## Slide 1: Introduction to Modelling of Cyber-Physical Systems (CPSs)
Peter Gorm Larsen, Aarhus University
together with
Hugo Macedo, Jalil Boudjadar, Stefan Hallerstede,
Casper Thule, Aarhus University
Ken Pierce, Carl Gamble, John Fitzgerald,
Newcastle University
Claudio Gomes, Antwerp University

## Slide 2: What is a Cyber-Physical System?
Systems of interacting systems
  Computing elements
  Physical elements
  Human interactions
Complex, networked character
Distributed control
Error detection and recovery

## Slide 3: Our position in a nutshell
We advocate:
Cyber-Physical Systems Engineering
  The product is a system: software is not the end!
Multidisciplinary collaborative modelling
(Co-) simulation as well as verification
  Promotes Design Space Exploration
  Entails well-founded co-simulation orchestration
Our approach:
Co-simulation of multiple Discrete Event and Continuous Time models
A tool chain – not single tools
  Requirements and Architectural models (in SysML)
  Traceability support through development
FMI interfaces constituent models
Semantic foundations in Unifying Theories of Programming

## Slide 4: What is Co-simulation?
Simulation of a system
Coupling of multiple simulators
Optionally as black-boxes
Each simulating one or more models
Built with different formalisms/tools.
Co-simulation scenario
Description of the system
The simulators and their dependencies
Data about the capabilities of each simulator.

## Slide 5: Remote Black-box Simulators
Suppliers make a simulator available through an API
Integrator takes care of programming an interface
Good IP Protection
Different suppliers require different interfaces

## Slide 6: Functional Mock-up Interface Standard
Simulator and model exported as a standardized C library
Standard interaction with any simulator
Every simulator is a black box.
Executed locally but can communicate with a remote server

## Slide 7: Inside an FMU
FMU
FMU
Model
Solver
Compiled
Model
Symbolic Info
Solver
FMU
Real or Simulated

## Slide 8: A New Toolchain for CPS Design

## Slide 9: INTO-CPS Unique Selling Points
Faster route to market for engineering CPSs
Avoiding vendor lock-in by open tool chain
Exploring large design spaces efficiently
Limiting expensive physical tests
Enabling traceability for all project artefacts

## Slide 10: CPS Engineering Needs
Enable collaboration across disciplines
Keep development costs low
Keep time-to-market short
Explore the complex design space efficiently
Ensure tolerance against “nasty” faults
Build up documentation for the working solution
Provide confidence to external stakeholders

## Slide 11: Outline Work Flow
Requirements Engineering
Construct SysML Architecture
Develop Simulation Models
Create FMUs
Select Library FMUs
Connect Multi-model
Simulation (single / DSE)
Model Checking
Hardware/Software in the loop
Results
Entry point 2
Entry point 1

## Slide 12: The INTO-CPS Tool Chain
Result
Result
Result
20-sim 4C
20-sim
Overture
OpenModelica
Modelio
Application
FMU
FMU
FMU
FMU
FMU
FMU
FMU
Configure / launch
  Co-simulation
  Design Space Exploration
  Model Checking
  Test Automation
View Results
Traceability
Model Descriptions
Traceability Daemon
RT-Tester
export
code
imports
COE (Co-simulation Orchestration Engine)
exports
configures
co-simulate
oracle
HiL
generates
Result
configure
launch
gather

## Slide 13: Co-simulation engine
Fully FMI 2.0 compliant Master Algorithm
Support for discrete event (DE) and continuous time (CT) models, using proposed FMI extensions
Multi-platform, 32/64 bit (Java-based)
Application based on Electron (web-technology)
Fixed and variable step size algorithms
FMI 2.0 Import/Export created for Overture, OpenModelica, 20-sim
Has also been tested with:
  Dymola
  Modelon FMI Toolbox for MATLAB/Simulink
  4DIAC
  SimulationX
  Unity

## Slide 14: INTO-CPS Methodology
Requirement Engineering
Architectural Modelling
Simulation Modelling
Analysis

## Slide 15: Architectural Modelling
Requirement Engineering
Architectural Modelling
Simulation Modelling
Analysis
Architecture Structure Diagram
Connections Diagram

## Slide 16: Simulation Modelling
Requirement Engineering
Architectural Modelling
Simulation Modelling
Analysis
“DE-first” approach, used in IPP4CPPS
  Model and test entire system in DE
    One class per EComponent, both DE and (abstract) CT
    Use Ether pattern to connect classes if necessary
  Move to multi-model
    One project per EComponent (link class definition)
    Export FMUs
1.
2.

## Slide 17: Design Space Exploration
Exhaustive
Taguchi Methods
Space Culling
Genetic Methods
How to Explore?
How to Assess?
DSE Driver
Simulation parameters, control of process
Objective Evaluator
Objective measures and constraint satisfaction from raw simulation results
Ranking
Ranking designs according to objective values
Presentation
Display of results and search progress to the user

## Slide 18: Example DSE Analysis
Requirement Engineering
Architectural Modelling
Simulation Modelling
Analysis

## Slide 19: Co-Simulation Foundations
Initial foundations developed for
  SysML
  VDM-RT
  Modelica
  FMI
SysML CPS profile defined
  Architecture Structure Diagram
  Connections Diagram
  Design Space Exploration Diagram
  Support for units in the exported model descriptions

## Slide 20: Common Semantics using UTP

## Slide 21: Underlying Unified Semantics

## Slide 22: INTO-CPS SysML CPS Profile
Three-tank Water Tank : INTO-CPS technology
  Design architecture using INTO-CPS profile
Architecture Structure Diagram comprised of three subsystems, corresponding to the three FMU models in the multi-model
Connections Diagram shows the connections between the different subsystems, and also their internal connections.

## Slide 23: DSE Views in the SysML Profile

## Slide 24: Cloud: Condor Exhaustive Search
Straggler handling:
return results when 80% of simulations complete or time > timeout

## Slide 25: Industrial Case Studies

## Slide 26: Industrial Follower Group
AGCO, Denmark
Airbus, UK
Alcatel Lucent, Ireland
Almende, Netherlands
Alten, Sweden
Altran, UK
Andritz Hydro, Austria
Bachmann Electronic, Netherlands
Bakker-Sliedrecht, Netherlands
Bang&Olufsen, Denmark
Beia Consult, Romania
Beumer, Denmark
Bombardier, Germany
Bosch, Germany
Carrier, France
CCFE, UK
CeTIM, Netherlands
Chemring Technology, UK
Conpleks Innovation, Denmark
Continental, Romania
Critical Software, Portugal
Daimler, Germany
Danish Aviation, Denmark
Dassault Aviation, France
Delphi, Poland
Denso Corporation, Japan
Dredging International, Belgium
DSTL, UK
EDF, France
Enginsoft, Italy
European Space Agency, Netherlands
Fortiss, Germany
Goodrich, UK
Grundfos, Denmark
GN Resound, Denmark
HADATAP, Poland
Holonix, Italy
HMF, Denmark
Huisman Equipment, Netherlands
IBM, Israel
IBM, Finland
Ikergune, Spain
Inestec, Portugal
Irmato, Netherlands
ISMB, Italy
Jaguar, UK
John Deere, Germany
JNE Systech, Korea
MAN Diesel & Turbo, Denmark
MFAtech, UK
NII, Japan
Nupark Accelerace, Denmark
Odego, Germany
OFFIS, Germany
Omflow, UK
ONERA, France
Oticon, Denmark
Phillips MRI, Netherlands
PLM Consult, Denmark
Polar Electro, Switzerland
Postech, South Korea
Prime Solutions Group, USA
Projectglobe.com, UK
Rockwell-Collins, France
Rolls-Royce, UK
Saab, Sweden
Santer Reply, Italy
Seluxit, Denmark
Siemens, Sweden
Synelixis Solutions,Greece
Syntell, Sweden
TailSiT, Austria
Tecnalia, Spain
Terma, Denmark
Thalès R&T, Germany
TTTech, Austria
thyssenkrupp Marine Systems, Germany
UTC Aerospace, UK
Vesta System, France
West Consulting, Netherlands
In total: 80

## Slide 27: The INTO-CPS Association Created
Purposes
Maintain and develop further software that was created in the project
Enable the widespread use of the software through open source licenses
Promote its usage in academic and industrial settings
Allow members to steer direction of development and incorporate software into products

## Slide 28: INTO-CPS Association - Technologies
SysML profile
Abstract modelling of CPS
Builds on top of the Modelio tool (Open Source)
Export of configurations for multi-models and DSE
Traceability support
Co-Simulation Orchestration engine
FMI 2.0 compliant master algorithm
Supports Windows, Linux, Mac
Parallelization and distribution support
Design Space Exploration tools
Algorithms for defining DSE runs and ranking the results
Uses DSE configurations from Modelio
Integrates well with the INTO-CPS application
INTO-CPS application
User Interface for setting up and executing Co-Simulation runs
Integrates many elements of the INTO-CPS tool chain
3D Animation FMU
Unity support for FMU 3D animation
INTO-CPS Traceability deamon
Using OSLC to track updates from all tools

## Slide 29: INTO-CPS Association - Licencing
General public | View source-code Use software for non-commercial purpose
Associated members | In addition: use software for commercial purpose
Silver members | In addition: voting rights at General Assembly
Gold members | In addition: combine software with own software for commercial purpose, without the need to publish the code when

## Slide 30: Hardware-in-the-Loop (HiL) and Code Generation
Functional Mock-up Interface
DE Model
CT Model
CT Model
DE Model
Multi-model
HiL
Code Gen.
Code Gen.

## Slide 31: Oculus Rift and Simulation

## Slide 32: Seeing a Product before it exists

## Slide 33: Test Automation
Based on RT Tester tool suite
Status:
  Test sets generated from XMI import (from Modelio)
  Test procedures are generated as FMUs, connected to Co-simulation
Outlook:
  Identify SuT in SysML profile, connect to Test Automation
  Connect SysML requirements with LTL formulas

## Slide 34: Model Checking Capabilities
Now finding shorter counter examples.
Integration of traceability.
Provides abstractions for CT signals:
  Interval-based abstraction
  Simulation-based abstraction (new)
  Gradient-based abstraction (new)

## Slide 35: Simulation-based abstraction
During model checking a CT variable should behave similar to a previous concrete execution of the entire system.
Extract signal flow from a test-run.
Signal flow is abstracted by a succession of interval abstractions.
Specify max allowed size of intervals to adjust granularity.

## Slide 36: Abstraction by Interval Boxes

## Slide 37: Gradient-based Abstraction
Allow CT variable to increase/decrease only up to a certain amount per time.
Implemented by a simple DE state machine.
s0
entry:
v = random(0, 20)
s1
entry:
v += random(0, 5)
t.elapsed(10)

## Slide 38: Traceability & Provenance
Goal: Ensure tracing between requirements, models, results, code
Keep track of changes
Use OSLC / Prov-N standards
Application
Traceability manager
Modeling / Simulation tool
Traceability plug-in
Repository / Database
COE

## Slide 39: Traceabilty – tool support
Modelio
OpenModelica
Overture
20sim
RT Tester
INTO-CPS App
Requirements creation / linking with SysML blocks
Architecture modelling
ModelDescription.xml export
Configuration export
ModelDescription.xml import
Model creation / modification
FMU export
Configuration to Multi-Model
Multi-model to COE configuration
Simulation
Define test model
Define test objectives
Run test
Define MC model
Define CT abstraction
Run MC query

## Slide 40: Traceability – multi-user support
Each message is a single plain text file (*.dmsg)
Messages are committed to common repository
Each user can generate messages

## Slide 41: Solutions for CPS Engineering Needs
Enable collaboration across disciplines
  Collaborative well-founded tool chain
Keep development costs low
  Lower need for physical tests by virtual co-simulation examination
Keep time-to-market short
  Enable concurrent engineering and gradual integration
Explore the complex design space efficiently
  Using Design Space Exploration
Ensure tolerance against “nasty” faults
  Experiment with what-if scenarios in a virtual setting
Build up documentation for the working solution
  Using combination of ad-hoc and automated tests
Provide confidence to external stakeholders
  Traceability between all project artefacts